## Slide 1
Resource Adequacy in the Pacific Northwest
Frank Afranji
Engineers for a Sustainable Future
May 11, 2021

## Slide 2
The Northwest Power Pool (NWPP) Corporation assures Member organizations achieve maximum benefits of coordinated operations
Core values: customer-driven, relationship-based, independent and operating with great integrity
What is the Northwest power pool

## Slide 3
The NWPP Membership is a voluntary organization and is made up of the following members:
Members include:
Alberta Electric System Operator, Avangrid, Avista, BANC, BC Hydro,BPA, Calpine, Chelan PUD, Columbia Grid, Cowlitz PUD, Douglas County PUD, Energy Keepers, Inc. EWEB, Fortis BC, Grant PUD, Grid Force, Idaho Power, NaturEner, NorthWestern Energy, NV Energy, PacifiCorp, Pend Orielle PUD, Perennial Power, PGE, Powerex, Excel Energy, PSE, Seattle City Light, Snohomish PUD, Tacoma Power, TID, US Army Corps, Bureau of Reclamation, Western Area Power Administration
What is the Northwest power pool

## Slide 4
Reliability is the NWPP focus

## Slide 5
Coal retirements – losing firm resources when the region already has relatively tight load-resource balance
  3,000 MW of coal resources will come offline in the next two years
New state policies demand a shift to a cleaner electricity supply portfolio
  Oregon Senate Bill 1547 increased the state’s RPS to 50% in 2016
  Washington Senate Bill 5116 established goals of carbon neutrality in 2030 and carbon-free by 2045
Utilities acting on their own – combination of policy and economics
  Avista and Idaho Power have pledged 100% clean electricity by 2045
  PacifiCorp, PSE, Idaho Power proposing early retirements of coal
A region in Transition

## Slide 6
The Northwest Power Pool was established in 1941 and since that time has been coordinating resources to maximize efficient electricity production
The NWPP today coordinates a number of different programs essential to the reliable operation of the NW power grid including:
  Reserve sharing program
  Pacific Northwest Coordination Agreement
  Western Frequency Response Sharing Group
  Training
Why Northwest power pool

## Slide 7
Multiple studies agree that the NW is approaching a period of capacity shortfalls
US WECC Coal Retirement Scenarios
NW Capacity Surplus / Deficit in Recent Studies
Note: WECC also publishes a resource adequacy assessment, but it focuses only on summer, whereas resource adequacy is primarily a winter issue for the Northwest
Note: Coal retirement scenarios developed by NWPP IRP Team. From research of announced and potential retirements from across the US WECC.

## Slide 8: How did we get here
The NWPP report: Exploring a Resource Adequacy Program for the Pacific Northwest, 2019 identified planning deficiencies in NWPP’s footprint
  Planning is state- and utility-specific
  Planning entities use different standards and methods
  As a result, the region lacks insight into its overall resource situation
As a result of the 2019 Report, NWPP and its member utilities are moving forward to design a regional RA program for NWPP members

## Slide 9: IRP needs assessment method
Chart: Weighted by peak load
| Deterministic (L/R balance) | Mixed | Percentile | LOLP | 1-in-10* | Other/unknown stochastic
 | 3110 | 10760 | 3040 | 16000 | 16820 | 1590
Chart: Weighted by number of utilities
| Deterministic | Mixed | Percentile | LOLP | LOLH | Other stochastic
 | 5 | 1 | 2 | 3 | 2 | 2
Data from IRP survey. Missing data filled in when possible.
Notes: 1-outage-in-10 years: Stochastic/probabilistic analysis.
2 of 3 utilities using an annual 2.4 hr LOLH target
1 public utility surveyed using 1-in-10 metriv
When viewed by peak load share, 1-outage-in-10 years and LOLP grow in popularity, largely at the expense of deterministic planning
Loss-of-load probability: Stochastic/probabilistic analysis.
2 utilities targeting 5% annually, 1 targeting 0.1 days per year
All IOUs doing some type of stochastic/probabilistic analysis
Percentile: P5 or P10 conditions (mix of hydro, loads, etc), often created via Monte Carlo simulation
Deterministic: Load/resource balance using fixed assumptions. May look at multiple metrics (annual energy, monthly energy, etc)
All utilities conducting deterministic or percentile planning are publics and hydro dominant. Most utilities looking at these metrics are concerned with energy as well as capacity.

## Slide 10: Wind & solar peak contribution varies
Missing data excluded. Blanks are zeros.
Depends on:
Location
Season of stress
Existing portfolio
Analysis method
Notes: Location:
Some areas are sunnier and/or windier
Season/hour of stress:
Summer vs. winter
Is the sun set or still up
Existing portfolio:
1st MW or 1,000th MW
is there storage, etc.
Analysis method:
LCC, 90th percentile, etc.

## Slide 12
Load Diversity
Resource Diversity
 | Winter | Summer
Noncoincident Peak | 80,000 MW | 86,000 MW
Coincident Peak | 76,000 MW | 84,000 MW
Approximate Estimated Load Diversity | 4,000 MW | 2,000 MW
Approximate Estimated Resource Diversity (3% NCP) | 2,400 MW | 2,600 MW
Total Diversity | 6,400 MW | 4,600 MW
Diversity Benefits
Two main forms TTW Two Main Forms TT

## Slide 13: Key program design elements
                Adequacy/Reliability metric
                Governance
                Program operation and monitoring
                Supply/demand forecast metrics
                Resource eligibility
                Deliverability requirements
                Capacity determinations
                Outage rates
                Import qualifications

## Slide 14: Benefits of a regional RA program
TRANSPARENCY
Regional approach to RA can inform a more comprehensive solution
Consistent standards among members
EFFICIENCY
Opportunity to access diversity benefits
CONFIDENCE
Confidence in regional RA needs

## Slide 15: Overview of Project Timeline

## Slide 16: Thank you!
https://www.nwpp.org/resources/